Analysis of Fireworks for Particles of the Type Found in Primer Residue (GSR)

Since 1977 and the "Aerospace Final Report on Particle Analysis for Gunshot Residue Detection," forensic scientists have called particles containing lead, barium, and antimony unique to primer residue. In September 1998, an article was published in the Canadian Society of Forensic Science Journal by Mosher, McVicar, et al., entitled "Gunshot Residue-Similar Particles Produced by Fireworks."  This study found non-spheroidal Pb,Ba,Sb particles in devices labeled “crackering balls.” These findings prompted further study in the analysis of over-the-counter fireworks for particles of the type found in primer residue (GSR).

The Midwestern Association of Forensic Sciences provided a grant to analyze several fireworks for the presence of particles similar to those found in primer residue.  For this study, 148 different fireworks were purchased in Ohio and Tennessee. Many of the Ohio fireworks were donated by the Rossi family fireworks company.  An attempt was made to purchase a wide variety of firework types that are commonly used.  In addition, particular effort was given to obtaining items labeled “crackles” or “crackering” because this effect could be generated by the presence of lead oxides.

There are many uses of lead, barium, and antimony in pyrotechnics, however, combinations of the three elements are not common.  The WIZards Pyrotechnic Formulary contains over 2400 pyrotechnic formulations (besides some primer formulations).  Only 49 of the more than 2400   contain Ba,Sb, 14 contain Pb,Ba, and only 3 contain Pb,Sb.  Lead chromate is used as an oxidizer, in delays, and to give a crackling effect.  Barium nitrate and barium chlorate are commonly used to produce green flames, as well as being used as oxidizers.  Antimony trisulfide is used as a fuel, as a source for white flame, and occasionally in flash and sound devices.

A sample of each firework was cut open, and the separated unburned ingredients were each examined by scanning electron microscopy energy dispersive x-ray spectrometry (SEM/EDX). This was done with the belief that if lead, barium, or antimony were not in the original ingredients they wouldn’t be in the burned residues.  Most of the unburned samples were analyzed by Dennis Ward of the Federal Bureau of Investigation Laboratory.  Most of the elements identified in the bulk powders from the unburned samples were found in the burned residues as well.  There were a few cases, however, where lead, barium, or antimony showed up in burned residues and not in the unburned ingredients.  One possible explanation for this might be an ashing effect.  Because most organics are burned away, inorganic elements would remain.       It may be of interest to note that only seventeen of the unburned ingredients had two of the three elements (Pb,Ba,Sb) contained in the powders.  And all but fifteen had magnesium somewhere in the mixture.  See the index at the end of the article.

In addition, a sample of each firework was set off, and burned residue from each was examined by SEM/EDX. In each case an attempt was made to obtain any residue that a person could possibly get on their hands when igniting the firework or when picking up its remains.  In a few cases, as in sparklers, the adhesive lifter was held close to the device as it went off.  In almost all cases, the lifter was pressed to the outer surface of the spent device and to residue from the device that was dumped onto a clean white sheet of paper.

Each sample was analyzed at the Hamilton County Coroner’s Laboratory with a Zeiss DSM 960A and Oxford EDX system.  An automated GSR run was performed first at 300X, followed by some manual observations in SE and BSE with a working distance of 15mm.  The samples were then analyzed a second time by John Giacalone at the West Virginia State Police Laboratory with a Camscan Series II and/or Tracor Northern 5500 instrument with a working distance of 31mm and magnification of 400X.

A total of 148 samples were tested.  Several different types of fireworks were tested to include a wide range of devices and to determine if any conclusions could be made about certain types being more or less likely to have GSR-like particles in their residue.  The category types and elements found are listed in Table 1.

The manual search of each lifter was performed to get an overall feel for the type of particles in the residue and to specifically look for particles with a spheroidal shape like those so often found in primer residue.  Sixty-eight of the 148 samples had particles in the 1um to 5um size range with a spheroid shape.  At the end of this article you will find an index with the name of the devices tested, their type, the elements lead (Pb), barium (Ba), and antimony (Sb) found in each before burning and in their residues after igniting, and in which residues morphological GSR-like particles were found.  Please note that this index only lists Pb,Ba,Sb, and Mg, but is not a comprehensive list of all of the various types of elements found in the residue particles.  A comprehensive list of all of the particles and their elements found in firework residues is compiled on a CD-ROM mentioned at the end of this article.

| Quantity | Type of Firework Device | Number in which characteristic GSR were found |
| --- | --- | --- |
| 19 | Fountains | 4 | Pb,Ba |
| 18 | Multiple shots | 3 | 2-Pb,Ba or 1-Pb,Sb |
| 18 | Bottle rockets | 3 | Pb,Sb |
| 13 | Ground animals | 0 |  |
| 12 | Ground spinners | 2 | 1-Pb,Ba or 1-Pb,Sb |
| 10 | Flying spinners | 0 |  |
| 10 | Firecrackers | 0 |  |
| 7 | Mortars | 0 |  |
| 7 | Roman candles | 0 |  |
| 6 | Wheels | 1 | Pb,Sb |
| 5 | Missile rockets | 1 | Pb,Sb |
| 5 | Smokes | 0 |  |
| 3 | Crackering balls | 3 | Pb,Ba |
| 3 | Sparklers | 0 |  |
| 3 | Snaps or poppers | 0 |  |
| 2 | Strobes | 1 | Pb,Ba |
| 1 | Snake | 0 |  |
| 1 | Parachute | 0 |  |
| 1 | Igniter | 0 |  |

TABLE  1.  Categorized firework devices and number of characteristic GSR particles found.

At least one of the three elements were contained in 117 of the residues.  It was no surprise that barium (Ba) was found to be very common in firework devices. It occurred in 105 residues. Lead (Pb) was found in 46 pyrotechnic residues.  Antimony (Sb), however, was only found in nine of the residues.  Other common elements found in pyrotechnic burned residue particles were potassium (K-almost always found), chlorine (Cl), sulfur (S), silicon (Si), magnesium (Mg),  or aluminum (Al). Quite often calcium (Ca), copper (Cu), or iron (Fe) were found.  And occasionally titanium (Ti), strontium (Sr), or zinc (Zn) were found.

Twenty-nine of the 148 residues were found to contain particles in which two of the three elements (Pb,Ba,Sb) were present.  Eleven of those 29 would not be confused with characteristic GSR particles on the basis of morphology or the presence of magnalium.  Magnalium is a 50/50 mixture of Al3Mg2 and Al2Mg3.  It is used because it is more stable than magnesium and produces attractive white sparks, a crackling effect similar to SbS3, and a branching spark effect when used with a black powder.  According to the Aerospace Report the presence of magnesium in a particle eliminates it as being from primer residue.  Therefore, out of 148 firework devices 18 were found to have particles containing Pb,Ba or Pb,Sb that were consistent in morphology with characteristic primer residue particles.  None were found to have all three elements in one particle as is necessary to be considered unique to primer residue particles.

While, at the present time, the league of forensic primer residue examiners have not discovered a small spheroid particle containing Pb, Ba, and Sb in anything other than primer residue, we are getting dangerously close.  It is not out of the realm of possibility that in the near future someone will find such a particle in residue from a pyrotechnic device or brake pads.  At that time we will not be able to use the word unique when referring to such particles coming from primer residue.  However, studies like this and others, while trying to disprove the uniqueness of such particles are actually strengthening our confidence in the rarity of such particles to sources other than primer residue.

For the past two years the Hamilton County Coroner’s Laboratory has had the submitting police agencies use a Tri-Tech GSR kit with the following questions on the information form:  “Has subject recently exploded or touched any used firework device:                                     	yes      no    If yes, what specific type was touched?”  To date, 221 kits have been submitted in which these questions were answered.  It is interesting to note that  200 times (90%) the subject answered “No.”   When the subject answered “yes” the specific type given was usually a generic answer, like M-80’s, firecrackers, or bottle rockets.  Of those 21 cases eight of the SEM/EDX results on the lifters were negative, but most of the positive samples were obvious primer residue with several Pb,Ba,Sb small spheroid particles.

A CD-ROM was compiled with all of the data in this project.  The data is arranged in PowerPoint slides.  Each slide contains a picture of the device, the name and type of device, the pyrotechnic effect, the inorganic contents of each unburned substrate in the device, a micrograph of a particle found in the residue, an EDX spectrum of a particle found in the residue, what was found on a normal run for GSR on the residue, the morphology of particles found, and finally, the elements identified within particles found in the burned residue of the device.

The Midwestern Association of Forensic Sciences paid for the distribution of over 100 of these CD’s to colleagues all over the world.  If you have not received a CD and would like to obtain one, please send $5.00 to:

Michael A. Trimpe

Hamilton County Coroner’s Laboratory

3159 Eden Avenue

Cincinnati, Ohio  45219

Mosher, P.V., McVicar M.J., Randall E.D., and Sild E.H., “Gunshot Residue-Similar Particles Produced by Fireworks,” Can. Soc. Forensic. Sci. J. Vol. 31. No. 2 (1998) pp. 157-168.

Wolten, G.M., Nesbitt, R.S., Calloway,A. R., Loper, G. L., and Jones, P. F., Equipment systems improvement program – final report analysis for gunshot residue detection, Rep. ATR-77 (7915) –3, The Aerospace Corporation., Washington, D. C., Sept. 1977.

Haarmann, Donald J., The WiZards Pyrotechnic Formulary, 1996 Edition.

Conkling, John A., Chemistry of Pyrotechnics, Marcel Dekker, New York, 1985.

Schwoeble, A.J., Exline D.L., Current Methods in Forensic Gunshot Residue Analysis, CRC Press Boca Raton, FL., 2000. pp.16-17.

Giacalone, John, “Forensic Fireworks Analysis and Their Residue by Scanning Electron Microscopy/Energy Dispersive Spectroscopy,” SCANNING Vol. 20, 3 April Meeting Proceedings (1998).

Kosanke, K.L. and B.J., “Pyrotechnic Reaction Residue Particle Identification by SEM/EDS,” Journal of Pyrotechnics. Issue 13 Summer 2001. pp. 40-53.

INDEX

|  | Name of Device | TYPE | Elements Found Unburned | Elements Found Burned Residue | GSR Morphology |
| --- | --- | --- | --- | --- | --- |
| 001 | Whistling Moon Travelers | Bottle Rocket | Ba Mg | Pb, Sb | Yes |
| 002 | Premium Moon Travelers | Bottle Rocket | Pb Sb Mg | Pb, Sb | Yes |
| 003 | Hellzacracking | Crackering Ball | Pb Mg | Pb, Ba | Yes |
| 004 | Crackering Ball | Crackering Ball | Pb Ba Mg | Pb, Ba | Yes |
| 005 | Sidney 2000 | 10 Shot | Pb Ba Mg | Pb |  |
| 006 | Cuckoo | Fountain | Ba Mg | Pb,Ba, Mg,Al | Yes |
| 007 | Birds of Triumkh Fountain | Ground Fountain |  |  |  |
| 008 | Plane Drops Parachute | Flying Spinner | Ba Mg | Ba | Yes |
| 009 | Bomber | Flying Spinner | Ba Mg | Pb or Ba |  |
| 010 | Golden Fish | Ground Animal | Ba Mg | Ba | Yes |
| 011 | Shogun Cone Fountain Silver | Fountain | Ba Mg | Pb or Ba |  |
| 012 | Shogun Cone Fountain Crackling | Fountain | Pb Mg | Ba |  |
| 013 | Multi-Color Shogun Fountain | Fountain | Ba Mg | Pb |  |
| 014 | Vulcan Wild Fire Fountain | Fountain | Ba Mg | Pb,Ba, Mg,Al | Yes |
| 015 | Krakatoa | Fountain |  | Pb, Ba | Yes |
| 016 | Brothers Fine Champagne Fountain | Fountain | Mg | Pb or Ba | Yes |
| 017 | Spring Of Youth Fountain | Fountain | Pb Ba Mg | Pb, Ba | Yes |
| 018 | TriangleWhistling Flower Firework | Fountain | Ba | Ba |  |
| 019 | Dragon Rocket | Bottle Rocket | Ba Mg |  |  |
| 020 | Thunder Rocket | Bottle Rocket | Ba Mg |  |  |
| 021 | Air Manderine Rocket | Bottle Rocket | Mg | Pb or Ba |  |
| 022 | Silvery River Rocket | Bottle Rocket | Ba Mg | Ba |  |
| 023 | Meteorite Rain | Bottle Rocket | Ba Mg |  |  |
| 024 | Fluttering Butterflies | Bottle Rocket | Ba Mg | Ba |  |
| 025 | Twilight Glitter | Bottle Rocket | Ba Mg |  |  |
| 026 | Cosmic Rain | Bottle Rocket | Mg |  |  |
| 027 | White Strobe | Bottle Rocket | Ba Mg | Pb, Ba |  |
| 028 | Yellow Bees | Bottle Rocket | Mg | Pb or Ba |  |
| 029 | White Bees | Bottle Rocket | Ba Mg | Ba |  |
| 030 | Red Bees | Bottle Rocket | Mg |  |  |
| 031 | Green Bees | Bottle Rocket | Ba Mg | Pb or Ba |  |
| 032 | Silver Whistling Candle 8 Shot | Roman Candle | Ba Mg | Ba |  |
| 033 | Vulcan National Salute 5 Ball | Roman Candle | Pb Ba Mg | Pb or Ba | Yes |
| 034 | Vulcan Smart Candle 5 Balls | Roman Candle | Ba Mg |  | Yes |
| 035 | 10 Guns Liling Salute | Roman Candle | Mg | Ba | Yes |
| 036 | Colored Shots | Roman Candle | Pb Ba Mg | Pb, Ba |  |
| 037 | 10 Balls Liu Yang Candle | Roman Candle | Ba Mg | Ba |  |
| 038 | No. 200 Crackling de Light | Mortar | Pb Ba Mg |  | Yes |
| 039 | Howling Tiger 25 Shot | 25 Shot | Ba Mg | Ba | Yes |
| 040 | Spaced Crusader 20 Shot | 20 Shot | Pb Ba Mg |  | Yes |
| 041 | Maucau 1999 25 Shot | 25 Shot | Pb Ba Mg | Ba |  |
| 042 | Battle of New Orleans | 25 Shot | Ba Mg | Pb, Ba | Yes |
| 043 | Twitter Glitter | Multiple Shots | Ba Mg | Pb or Ba | Yes |
| 044 | War Game 25 Shot | 25 Shot | Ba Mg | Ba | Yes |
| 045 | Mini Red Mountain | Multiple Shots | Ba Mg | Pb or Ba |  |
| 046 | Marti Gras Parade 25 Shot | 25 Shot | Mg | Ba | Yes |
| 047 | Gold Beach 37 Shot | 37 Shot | Mg | Pb, Ba | Yes |
| 048 | Saturn Missiles Battery 100 Shots | Missile Shots |  |  |  |
| 049 | Garden in Spring | Fountain & shots | Ba Mg | Ba |  |
| 050 | Explosion in Blue | 25 Shot | Pb Ba Mg |  |  |
| 051 | Cajun Pageant 25 Shot | 25 Shot | Ba Mg |  |  |
| 052 | Sidney Bridge | 25 Shot | Pb Ba Mg | Pb or Ba |  |
| 053 | Wheel of Fortune | Wheel | Ba Mg |  |  |
| 054 | Wheel of Vegas | Wheel | Ba Mg |  |  |
| 055 | Wheel of Luck | Wheel | No test | Ba |  |
| 056 | Colourful Wheel | Wheel | No test | Pb, Sb | Yes |
| 057 | Davey Fire Electric Igniter | Igniter | Pb Mg | Pb | Yes |
| 058 | Gold Sparklers | Sparklers | Ba | Ba | Yes |
| 059 | Cobra Black Snake | Snake | Ba | Ba |  |
| 060 | Pop Pop Snappers | Snaps |  |  | Yes |
| 061 | Twisting Tornado | Ground Spinner | Mg |  |  |
| 062 | The Mighty Dragon | Ground Animal | Mg | Ba |  |
| 063 | Europa I Missile | Rocket | Pb Ba Mg | Pb, Sb | Yes |
| 064 | Black Arrow Missile | Rocket | No test | Pb,Sb Mg,Al | Yes |
| 065 | Shogun Super Charged Firecracker | Firecracker |  |  |  |
| 066 | Silver Slug Cracker | Firecracker | Pb Ba Mg | Pb,Ba Mg,Al | Yes |
| 067 | Center Fire Cracker | Firecracker | Mg | Ba |  |
| 068 | Black Cat Firecracker | Firecracker | Mg | Ba | Yes |
| 069 | Thunder Bomb | Firecracker |  | Ba | Yes |
| 070 | Jumping Jack Firecracker | Small Firecracker | Ba Mg | Ba |  |
| 071 | Texas Rider | Ground Animal | Mg | Pb or Ba |  |
| 072 | Tank With Report | Ground Device | Mg | Ba | Yes |
| 073 | Shogun Ground Spinning Flower | Ground Spinner | Ba Mg | Ba | Yes |
| 074 | Phantom Cracklin’ Bloom | Ground Spinner | Pb Ba Mg | Pb,Ba Mg,Al | Yes |
| 075 | Starball Contibution | Ground Spinner | Ba Mg | Ba |  |
| 076 | Magic Ball Fireworks | Ground Spinner | Ba Sb Mg | Ba or Sb |  |
| 077 | Phantom Turbo Props | Ground Spinner | Ba Mg | Pb, Ba Mg | Yes |
| 078 | King Crab | Ground Spinner | Mg | Pb, Ba | Yes |
| 079 | Golden Goose | Ground Spinner | Mg | Ba |  |
| 080 | Turtle | Ground Animal | Ba Mg | Ba |  |
| 081 | Monkey Drive | Ground Animal | Ba Mg | Ba |  |
| 082 | Hen Laying Egg | Ground Animal | Mg | Ba |  |
| 083 | Fire Dragon | Ground Animal | Ba Mg | Ba | Yes |
| 084 | Signal Flare | Strobe | Ba Mg | Ba | Yes |
| 085 | Rhinoceros | Ground Animal | Mg | Pb, Ba Mg,Al | Yes |
| 086 | Rooster | Ground Animal | Ba Mg | Ba | Yes |
| 087 | Tiger Head Red Meteor Rocket | Bottle Rocket | Ba Mg | Ba | Yes |
| 088 | Screaming Dragon Rocket | Bottle Rocket | Pb Ba Mg | Pb, Ba |  |
| 089 | Texas Pop Rocket | Bottle Rocket | Mg | Ba |  |
| 090 | Yellow Rose Texas Rocket | Bottle Rocket | Pb Sb Mg | Pb, Sb | Yes |
| 091 | Peacock Classicx Rocket | Bottle Rocket | Ba Mg | Ba |  |
| 092 | Crackling Cactus | Crackering Ball | Ba Mg | Pb, Ba | Yes |
| 093 | Cracklin’ Strobe Light | Strobe | Ba Mg | Pb, Ba | Yes |
| 094 | Pro Magnum Silver to Crackle.et al | Mortar | Ba Mg | Ba |  |
| 095 | Dragon Spits Fire Fountain | Ground Animal | Ba Mg | Ba | Yes |
| 096 | Plum Flowers Report Spring | Fountain | Ba Mg | Pb or Ba | Yes |
| 097 | UFO | Ground Spinner | Ba Mg | Ba | Yes |
| 098 | 2 Cool Fountain | Fountain | Ba Mg | Pb, Ba | Yes |
| 099 | Four Performances | Fountain | Ba Mg | Ba |  |
| 100 | Sound of City Fountain | Fountain | Ba Mg | Pb, Ba | Yes |
| 101 | Silvery Water Fountain | Fountain | Ba Mg | Ba |  |
| 102 | 4” Conic Fountain | Fountain | Ba Mg | Ba |  |
| 103 | Double Parachute Night | Roman Candle | Ba Mg | Ba | Yes |
| 104 | Jump Shot | Shots | Pb Mg | Pb, Sb | Yes |
| 105 | Bad Bombs | Mortar | Pb Mg | Ba |  |
| 106 | Ole Time Shoot Out | Shots | Mg | Ba |  |
| 107 | Happy | 16 Small Shots | Ba Mg | Ba |  |
| 108 | Silver Chrysanthemum | Mortar | No test |  |  |
| 109 | Kalidescope | 8 Shots | Ba Mg | Pb or Ba | Yes |
| 110 | Parachute | Parachute | Ba Mg | Ba | Yes |
| 111 | Wailing Wheel | Wheel | Mg | Ba |  |
| 112 | Jumping Wheel | Wheel | Mg | Ba | Yes |
| 113 | Rainbow Wheel | Wheel | Mg | Ba | Yes |
| 114 | Spinning Wheel | Wheel | Mg | Ba |  |
| 115 | Champaign Party Popper | Popper |  |  |  |
| 116 | Magnum Pistol Popper | Popper |  | Ba |  |
| 117 | Mad Dog Firecracker | Firecracker | Mg |  |  |
| 118 | Lady Cracker | Firecracker | Mg | Ba |  |
| 119 | Cat Copter | Flying Spinner | Mg | Ba |  |
| 120 | Plane Flying At Night | Flying Spinner | Ba Mg | Ba |  |
| 121 | Space Flyer | Flying spinner | Ba Mg |  | Yes |
| 122 | Space Banger | Flying Spinner | Mg | Ba |  |
| 123 | Outer Space Craft | Flying Spinner | Ba Mg | Ba |  |
| 124 | Twisting Tornado | Flying Spinner | Ba Mg | Ba |  |
| 125 | Bootleg Bomber | Firecracker | Mg |  |  |
| 126 | Morning Glory Sparklers | Sparklers | Ba Mg | Ba | Yes |
| 127 | Black Cat Sparklers-Black Gold | Sparklers | Ba | Ba | Yes |
| 128 | Blockbuster Firecrackers | Firecrackers | Mg |  |  |
| 129 | Cracklin’ Ground Bloom | Ground Spinner | Ba Mg | Pb,Ba Mg,Al | Yes |
| 130 | Tasmanian Devils | Ground spinner | Ba Mg | Ba |  |
| 131 | Buzz Bombs | Flying Spinner |  |  | Yes |
| 132 | Camellia Flower | Ground Spinner | Mg |  |  |
| 133 | Lotus Firework | Ground Spinner | Ba Mg | Ba |  |
| 134 | Whistling Chaser | Ground Spinner | Mg | Pb, Sb | Yes |
| 135 | Whistling Gemini Missile | Missile | Mg | Ba | Yes |
| 136 | Whistling Jupiter Missile | Missile |  |  |  |
| 137 | Mammoth Smoke | Smoke | Ba | Ba | Yes |
| 138 | Showtime Mini Smoke | Smoke | Ba | Ba |  |
| 139 | “The Half Stick” Smoking Cracker | Smoke | Mg |  |  |
| 140 | Blockbuster Smoke Balls | Smoke | Mg | Ba |  |
| 141 | Smoke Grenade | Smoke | Mg | Ba |  |
| 142 | Nutty Monkey Fountain | Fountain | Ba Mg | Ba | Yes |
| 143 | ProMagnumDragonEggsWith Report | Mortar | Mg |  |  |
| 144 | Artificial Satellite | Flying Spinner | Mg | Ba |  |
| 145 | X Wing 8 Missile | Missile | Pb Mg | Ba | Yes |
| 146 | Four Color 1” Fountain | Fountain | Pb Mg | Pb | Yes |
| 147 | Rozzi 4” mortar | Mortar | No test |  | Yes |
| 148 | Rozzi 6” Mortar | Mortar | No test |  | Yes |
|  |  |  |  | 117 = 1 or more |  |
|  |  |  |  | 29 = 2 Pb,Ba or Sb | 68 |
|  |  |  |  | 18 = like GSR char |  |